## Slide 1: Channel Prediction and MCS Selection
Alka V N

## Slide 2: MCS SELECTION
Direct
Channel prediction

## Slide 3: MCS SELECTION in OFDM Systems
Optimizing data transmission efficiency and quality of service
This Paper Compared Many AI Algorithms for MCS Selection
AI Algorithms:
  Artificial Neural Networks (ANN), including a Deep Neural Network (DNN).
  Support Vector Machine (SVM).
  Random Forest (RF).
  Bagging with k-Nearest Neighbors (B-kNN).
Concluded that ANN with 2 hidden layers have 98.71% accuracy
Uses dataset from simulation
MCS SELECTION

## Slide 4: MCS SELECTION in OFDM Systems
Input Features :
  Signal-to-Interference-plus-Noise Ratio (SINR)
  Operating Frequency (F)
  BS Altitude (Ht)
  Path Visibility (V)
  Propagation Distance (D)
Output : MCS class ID (̂MCS), which determines the modulation and coding scheme to be used.
MCS SELECTION

## Slide 5: Link adaptation using MCS Correction (1)
Optimise traditional OLLA by RL to to achieve throughput maximization and Block Error Rate (BLER) minimization
Output: the offset that determines the effective SINR used for Modulation and Coding Scheme (MCS) selection
Dataset Used: synthetically generated data from the 5G simulation environment.

## Slide 6: Link adaptation using MCS Correction (1)
Input Parameters:
  Estimated Signal-to-Interference-plus-Noise Ratio (SINR) at gNB (γ̂m)
  Weighted ACK-NACK ratio until step t
  ACK-NACK value at the previous step
  Difference between the actual CQI reported by UE and the estimated CQI by gNB after offset correction at step t (∆Ct)

## Slide 7: Link Adaptation using MCS Correction(2)
Reinforcement Learning (RL) model to enhance the performance of the Outer-Loop LA (OLLA) by dynamically adjusting the UL Modulation and Coding Scheme (MCS) to increase throughput while maintaining a decent Block Error Rate (BLER)
Output parameter: correction factor that can be added to the MCS value chosen by the Inner-Loop LA (ILLA) to obtain the final MCS used for transmission
Dataset used for this research is based on a simulation environment developed using a professional simulation tool provided by Ericsson

## Slide 8: Link Adaptation using MCS Correction (2)
The input parameters to the proposed RL system are:
  The MCS value chosen by the scheduler for the UL transmission.
  A flag identifier indicating whether the transmission is a new transmission (set to 1) or a retransmission (set to 0), based on the UL HARQ Process ID
ACK/NACK flag sent by the receiver used for the reward function

## Slide 9: Convolutional Neural Network (CNN) to select the Modulation and Coding Scheme (MCS)
Uses CNN (Direct and Indirect based on)
  Direct Method: This approach uses a CNN with two convolutional layers and one fully connected layer. It is framed as a classification problem where the CNN directly predicts the MCS level from the past SNRs. The output layer uses a softmax activation function.
  Indirect Method: This approach employs a CNN with six convolutional layers and one fully connected layer. It is formulated as a regression problem where the CNN first predicts the future SNR, and then the appropriate MCS is selected based on this predicted SNR. The loss function used for training was mean square error (MSE)

## Slide 10: Convolutional Neural Network (CNN) to select the Modulation and Coding Scheme (MCS)
inputs and outputs of the AI models are:
  Input: A vector of past measured SNR values. The length of this vector is 50 for the direct method and 40 for the indirect method. The data is preprocessed using linear interpolation to handle missing SNR values
  Output (Direct Method): The selected MCS level. This is a discrete value representing one of the available MCS indices (0-6 as shown in Table I).
  Output (Indirect Method): The predicted SNR value for a future transmission time. This predicted SNR is then mapped to an appropriate MCS level based on the thresholds defined in the MCS table

## Slide 11: Convolutional Neural Network (CNN) to select the Modulation and Coding Scheme (MCS)
DataSet: The dataset used in this study is generated through computer simulations.
  The simulations consider both Rayleigh and Rician fading channels. The SNR is sampled every OFDM symbol.
  The simulations cover a range of SNR from 0 to 30 dB and mobile speeds from 0 to 100 km/h.
  The likelihood of recording received SNRs varied from 10% to 100%, and SNR recording periods were tested in increments of 10 from 10 to 100.
  The length of the past SNR data used as input was 50 for the direct and conventional methods, and 40 for the indirect method.
  The generated data was split into training (200,000 samples), validation (20,000 samples), and test (20,000 samples) sets

## Slide 12: Channel Prediction For MCS Selection
Output Parameter: The output of the proposed uncertainty-aware MCS selection algorithm is the selected Modulation and Coding Scheme (MCS) for the transmitter to use in the next data transmission phase
Method: using neural networks for channel prediction and then developing a robust MCS selection strategy based on the uncertainty inherent in these machine learning predictions
Dataset used :
  real world dataset: https://github.com/postman511/Wireless-Signal-Strength-on-2.4GHz-WSS24-dataset

## Slide 13: Channel Prediction For MCS Selection
For the channel prediction ANN
Input : a history of channel gain measurements up to the current time to predict future values (10 historical data points)
Ouput: prediction of future channel gain values

## Slide 14: Deep learning based Channel Prediction
The research aims to predict this fading channel coefficient (h) using a deep learning model
Note:
  In a conventional single input single output (SISO) wireless communication system, the received signal (y) can be represented by the equation y = hx + n.
    Here, h represents the fading channel coefficient, which characterizes how the transmitted signal (x) is affected by the wireless channel as it travels to the receiver.
    n represents the additive white Gaussian noise.
  h^2 is proportional to gain

## Slide 15: Deep learning based Channel Prediction
Dataset Used: For training the model, a sample dataset is generated through the open-source channel simulation software NYUSIM
Input Parameters: The proposed LSTM model uses a sequence input comprising:
  history of channel impulse response (CIR) data
  along with two other features viz.
    transmitter-receiver update distance
    root-mean-square delay spread values

## Slide 16: Questions
What is the Predicting Variable?
What other measurements can be used ?

## Slide 17: Thank you