## Slide 1: Thesis Progress 5GAI
Alka Valiparambil Narendran Supervisor: Prof Evgeny Osipov | Associated Company : Effnet AB

## Slide 2: introduction
Real-time link adaptation is critical in 5G networks for maintaining high throughput and reliable communication.
Rapid changes in channel conditions demand continuous adjustment of communication parameters.
Relying on traditional heuristic-based MCS selection often results in suboptimal performance in dynamic environments.

## Slide 3: What is Link Adptation in 5G?
Link adaptation in 5G networks refers to the process of dynamically adjusting transmission parameters, such as modulation, coding, and transmit power, to optimize the communication link between the base station (gNodeB) and the user equipment (UE). The goal of link adaptation is to maximize spectral efficiency, throughput, and reliability while adapting to changing channel conditions and user requirements.[1]

## Slide 4: Traditional Approaches
Inner Loop Link Adaptation (ILLA) - Adaptive Modulation and Coding (AMC)
Uses instantaneous SINR or CQI feedback from the receiver to select the best Modulation and Coding Scheme (MCS) based on a predefined lookup table.
Strengths: Simple, fast, and efficient in stable conditions.
Weaknesses: No memory of past errors; inaccurate if channel estimates (CQI) are wrong.
Outer Loop Link Adaptation (OLLA)
Adjusts an SINR offset dynamically using ACK/NACK feedback to ensure the target Block Error Rate (BLER) is met. Works on top of ILLA.
Strengths: Corrects errors in SINR estimation, improves reliability, and fine-tunes MCS decisions.
Weaknesses: Can be slow to converge in fast-changing environments and struggles with extremely low BLER targets (e.g., in URLLC).
Hybrid Automatic Repeat Request (HARQ) with AMC
Retransmits failed packets with additional coding redundancy (incremental redundancy or chase combining) while also adapting MCS dynamically to improve reliability.
Strengths: Provides error correction without requiring extra retransmissions, ensuring robustness while maintaining high throughput.
Weaknesses: Introduces extra latency due to retransmissions, which can be problematic in ultra-low latency applications.

## Slide 5: Link Adaptation Working(DL)
Reference Signals & CSI Request: The base station first sends out reference signals for the UE (user device) to measure the channel quality. It then requests Channel State Information (CSI).
CSI Report (CQI, RI, PMI): The UE responds with its measured CSI, which typically includes:
CQI (Channel Quality Indicator): Indicates how robust the channel is and which MCS could work.
RI (Rank Indicator): Suggests the number of MIMO layers the UE can handle.
PMI (Precoding Matrix Indicator): Recommends the precoding strategy.
DCI on PDCCH (Chosen MCS/Rank): Using the CSI, the base station decides the modulation and coding scheme (MCS), the transmission rank, and other parameters, then notifies the UE via the Downlink Control Information (DCI).
Data Transmission & HARQ Feedback: The base station sends user data on the downlink. After receiving and decoding it, the UE sends an ACK (success) or NACK (failure).
MCS Adjustment & Retransmission: If the UE reports a NACK, the base station may lower the MCS (if needed) and retransmit the data to ensure reliable delivery.

## Slide 6: What is BLER (Block Error Rate)?
BLER is the percentage of incorrectly received blocks in total transmitted blocks.
It is calculated as a running average over a window of past transmissions.
Helps in dynamically adjusting MCS to maintain reliable communication.

## Slide 7: Initial LAM and Adjustment Process
Initial LAM Value: Starts at -3.
ACK (Successful Transmission): LAM increases gradually.
NACK (Retransmission Needed):LAM decreases accordingly.
Adjustments ensure optimal MCS selection for network efficiency.

## Slide 8: BLER Targeting and Dynamic Adjustment
The system aims to keep BLER at 10%.
Since BLER is a running average, LAM adjustments are gradual.
If BLER drops below 10% → LAM increases to improve throughput.
If BLER rises above 10% → LAM decreases to stabilize quality.

## Slide 9: Adaptive LAM Behavior Around BLER Target
LAM continuously fluctuates around the 10% BLER threshold.
Adjustments are not immediate but responsive to long-term trends.
Ensures MCS is neither too aggressive nor too conservative.

## Slide 10: Summary of BLER and LAM Adjustments
Condition | BLER Calculation | LAM Adjustment
Startup | Initial calculation begins | LAM = -3
ACKs Dominate | BLER < 10% (too few errors) | LAM increases
NACKs Increase | BLER > 10% (too many errors) | LAM decreases
BLER ~ 10% | Balanced state | LAM fluctuates up/down

## Slide 11: Understanding HARQ and MCS Selection in DL & UL Based on Logs
HARQ Process and MCS Adjustment
The logs indicate how the system handles Hybrid Automatic Repeat reQuest (HARQ) in Downlink (DL).
Based on Acknowledgment (ACK) or Negative Acknowledgment (NACK), the Link Adaptation Mechanism (LAM) adjusts the Modulation and Coding Scheme (MCS) dynamically.
Transmission Type | ACK Action | NACK Action
Downlink (DL) | LAM +0.01 | LAM -0.01
Uplink (UL) | LAM +0.1 | LAM -0.1

## Slide 12: Downlink (DL) Behavior
ACK Received (Successful Transmission)
Example Log:
1740363206205417086 info HarqManager-DL(42000): Released HARQ-process 5
  Action Taken: LAM is increased by +0.01
    Result:
1740363206205417456 info UE(42000): MCS(DL): base: 19 LAM: 8.00008 index: 27
NACK Received (Retransmission Required)
Example Log:
1740363206215936216 info HarqManager-DL(42000): Retransmission for HARQ-process 5
Action Taken: LAM is decreased by -0.01
Result:
1740363206215936696 info UE(42000): MCS(DL): base: 19 LAM: 7.99008 index: 26

## Slide 13: Problem statement
This research aims to develop an AI-driven algorithm—potentially leveraging reinforcement learning techniques—to optimize MCS selection in real time. By intelligently adapting to instantaneous channel variations, the proposed solution seeks to maximize throughput efficiency, minimize error rates, and enhance overall network reliability.

## Slide 14: Objectives
RO1
RO2
RO3
Assess Computational Feasibility: Analyze the algorithm’s computational complexity and response times within the lab test bed to confirm its capability for near-real-time operation.
RO4
Validate Robustness Across Simulated Scenarios: Test the algorithm under a variety of simulated channel conditions to ensure consistent performance and adaptability in different network scenarios.
Develop a Reinforcement Learning Model: Design and implement an AI-driven algorithm that dynamically selects the optimal MCS based on simulated instantaneous channel variations.
Quantitatively Evaluate Performance in a Lab Test Bed: Demonstrate that the proposed algorithm improves throughput efficiency and reduces error rates compared to traditional methods, using a controlled lab test bed setup.

## Slide 15: Limitations of current data
Over a short period of time in ideal conditions.

## Slide 16: My Other DOCs
Google colab: https://drive.google.com/file/d/1H8Uduk2Hddb9q7AuAx3h1hubIfTi1hCA/view?usp=sharing

## Slide 17: Thank you